##### ECOMMS			 	Final Exam		             	   May 5, 2008

#### Spring 2008 							                    	1:00-3:00 PM

Student’s Name:

DIRECTIONS: This exam consists of three parts – Part A, Part B and Part C. Answer all questions in all three parts. This exam is OPEN TEXTBOOK/NOTES, CLOSED COMPUTER/WEB. Calculators are permitted. Remember to specify UNITS for all answers. Use proper NOTATION. Show ALL WORK. List ALL ASSUMPTIONS.

Part A (4 questions @ 10 points each = 40 points)

- Let the probability of occurrence of a message be p.

  - Plot the amount of information gained by the occurrence of this message as p varies from 0 to 1. Specifically indicate the values along the x- and y-axes for p = 0; p = 0.5 and p = 1.0.

  - Plot the contribution of the average information generated by the message to the total source entropy for varying values of p. Again, indicate the values along the x- and y-axes for p = 0; p = 0.5 and p = 1.0.

  - What observations can you make from the two plots that you have generated?

- The number of bits required to store text is much less than that required for storing its spoken equivalent. Explain the reason for this.

- What are the design considerations used in choosing the time-constant of an envelope detector so that it can successfully demodulate standard-AM signals?

- Describe a procedure for calculating the range of modulation indices of an ICL8038 Precision Waveform Generator/Voltage Controlled Oscillator that is used as a frequency-modulator.

Part B

- A dual-mode cell phone is designed to operate either in the 900-MHz band or in the 1.9-GHz band. The cell phone uses a superheterodyne receiver with a 500-MHz IF for both modes.

  - Calculate the LO frequency and the image frequency for high-side injection when the phone receives an 880-MHz signal.

  - Calculate the LO frequency and the image frequency for low-side injection when the phone receives a 1.960-MHz signal.

  - Discuss the advantages of using a 500-MHz IF for this dual-mode cell phone.

(20 points)

Part C

- Community Telephone Service

You are required to design a digital telephone service for a rural subdivision with about 400-subscribers. You are provided with 50 twisted-wire-pair lines in order to accommodate a maximum system length of 50-miles. The encoded VF signals are of telephone quality – i.e. the maximum audio frequency is limited to 4-kHz. The system you design must support full-duplex communications – i.e., both parties can talk and listen simultaneously to the other person. You are also required to conform to the North American digital TDM standards.

  - In beginning your design process, what level system in the TDM hierarchy would you choose? Why?

  - How many subscribers can be supported if all the 50 twisted-wire-pair lines are placed into service?

  - How many subscribers can be supported if 2 of the 50 twisted-wire-pair lines are reserved for spares?

  - What is your system data rate at full capacity?

(40 points)