##### ECOMMS			 	Quiz	1	             		Feb 17, 2009

#### Spring 2009 								     9:30 – 10:30 AM

Student’s Name: 								____________

DIRECTIONS: This quiz is CLOSED BOOK/NOTES/COMPUTER/WEB. Calculators are permitted. Remember to specify UNITS for all answers. Use proper NOTATION. Show ALL WORK.

- A digital communications channel has a bandwidth of 1 MHz and tolerates a maximum SNR of 7. What is the maximum data rate allowable in this system for error-free transmission and reception?

(5 points)

- The signal, m(t) = Amcos(2fmt) is

(a) An energy signal				(b) A power signal

(c) Both					(d) Neither

Give reasons for your answer.

(5 points)

- Write down the time-domain expression for the following frequency-domain signal:

S(f) = (f – 500) + (f + 500) + (f – 300) + (f + 300)

(5 points)

- Write down the characteristics of an ideal communications system.

(5 points)

- What is the Nyquist sampling rate for the following signal?

w(t) = sinc(200t)

(5 points)