## Slide 1: Green Roofs
Used for 1000s of years
  Cool buildings in Africa
  Retain heat for Vikings
www.2championroofing.com

## Slide 2: Types
Intensive
  Like a garden
Extensive
  Slow Growing, Stress-tolerant plants
Semi-Intensive
  In-between
cdnimg.visualizeus.com

## Slide 3: Intensive (6”+)
www.greenroofplan.com
150+ mm layer substrate
Plants, vegetables, shrubs, trees,…
Frequent maintenance needed
Heavy
Provide a “park” where land is too expensive
Green Roof Centre (2007) The Green Roof Pocket Guide, 2nd Ed.
Notes: 150+ from http://www.3riverswetweather.org/
Intensive: Intensive green roofs have greater than six inches of substrate. Intensive green roofs are particularly attractive for developers, property owners, and municipalities, in areas where land prices command a premium, but property owners want to provide some of the amenities associated with parks.

## Slide 4: Intensive
www.greenroofs.com
Baltimore Convention Center
Notes: Project Name: Baltimore Convention Center Year: 2010 Owner: City of Baltimore Location: Baltimore, MD, USA Building Type: Commercial Type: Extensive & Intensive System: Single Source Provider Size: 28000 sq.ft. Slope: 1% Access: Accessible, Open to Public Submitted by: Barrett Company & National Roofing Co. Designers/Manufacturers of Record: Architect: Chris Labosky, LEED AP, Gant Brunnett Architecture General Contractors: Chuck Sadowski, Project Manager, National Roofing Co., Inc. Waterproofing and Greenroof System Supplier: Barrett Company Greenroof System: Greenroof-Roofscapes? Technical Consultant: Barrett Company

## Slide 5: Intensive
www.greenroofs.com
Yale University
Smilow Cancer Hospital
Notes: Yale University Smilow Cancer Hospital, New Haven, Connecticut, USA! The following is an intensive green roof project we constructed last in 2009. This project is located on the seventh floor of the Yale University Smilow Cancer Hospital. It contains a 90 foot water feature as well as 3,200 sq. ft. of clay pavers. The architectural firm who designed this project was Towers Golde, Inc. Photo by Albert Leavitt

## Slide 6: Extensive (≤4”)
Sedum Roof
  20-100 mm substrate
    cuttings or plugs, or pre-grown mats
Meadow Roof
  70-100 mm substrate
  Dry habitat wildflower & grass seed mixes
Brown or Biodiversity Roofs
  Allow a natural habitat to develop
  Use crushed brick, leftover soils for substrate
Green Roof Centre (2007) The Green Roof Pocket Guide, 2nd Ed.
Notes: http://www.3riverswetweather.org/
Extensive: Extensive green roofs have four inches or less of growing medium.Extensive green roofs provide many of the environmental benefits of intensive green roofs, but they are designed to be very low-maintenance and are not typically designed for public access.

## Slide 7: Pre-Vegetated Mats
www.xeroflora.com

## Slide 8: Modular Trays High Museum of Art Atlanta, GA, USA 2008
www.greenroofs.com
Notes: Project Name: Frances Bunzl Administration Center of the High Museum of Art Year: 2008 Owner: High Museum of Art Location: Atlanta, GA, USA Building Type: Museum Type: Extensive System: Single Source Provider Size: 6680 sq.ft. Slope: 1% Access: Accessible, Private Submitted by: WESTON? Designers/Manufacturers of Record: Installation: WESTON? Planting Design Contributor: Savannah College of Art and Design Modular Greenroof System: GreenGrid? Plant Supplier: Saul Nurseries Growing Medium Supplier: ItSaul Natural

## Slide 9: Sedum
www.asla.org
Water Treatment Facility, New Haven, CT
30,000 ft2 green roof was largest in Connecticut in 2010
Notes: Wikipedia
Sedum is a large genus of flowering plants in the family Crassulaceae, members of which are commonly known as stonecrops. The genus has been described as containing up to 600 species [2] of leaf succulents that are found throughout theNorthern Hemisphere, varying from annual and creeping herbs to shrubs. The plants have water-storing leaves. The flowers usually have five petals, seldom four or six. There are typically twice as many stamens as petals.

## Slide 10: Modular Trays - Sedum
ww1.prweb.com

## Slide 11: Sedum
www.americanrivers.org
J.W. Winco (New Berlin, WI) 15,800 ft2 green roof
Captures >18,000 gallons during 1-inch rainfall event
Reduces heating and cooling, improves air quality, extends roof life
Notes: 2013 article
J.W. Winco is one of many businesses stepping up to make a difference in their local watershed. They are major supplier of standard industrial machine components in New Berlin, Wisconsin, and recently completed installation of a green roof system on its manufacturing facility.
MMSD funding covered 29% of the cost of the project. This 15,800 square foot green roof is now one of the largest in the state, and is capturing over 18,000 gallons of stormwater during a 1-inch event. The sedum used on the roof was grown locally by Hanging Gardens.
The green roof will now greatly reduce heating and cooling costs, lower energy usage, improve air quality, increase urban green space, extend the roof life and reduce J.W. Winco’s stormwater fee paid to the city. J.W. Winco is also working with American Rivers on retrofitting their 2 acre parking lot with a combination of bioswales and porous pavement in the coming year.
- See more at: http://www.americanrivers.org/blog/business-case-sustainability/#sthash.RPtmy2Lw.dpuf

## Slide 12: Meadow
greenroofmalmo.files.wordpress.com
Augustenborg Botanical Roof Garden, Malmo, Sweden

## Slide 13: Meadow
Home, California
cdn.c.photoshelter.com

## Slide 14: Brown
blog.emap.com
Lambeth, Central London, UK
Brown ruble substrate
Notes: Lambeth is a district in Central London, England
Brown roof above a meeting room at Roots and Shoots. Its aim was to improve local biodiversity. The roof has a substrate of brown rubble, and very little was actually planted; most of the green that can be seen on the roof has self seeded.

## Slide 15: Brown
Laban Dance Center, London England
Designed to encourage Black Redstart (bird)
plus.google.com
Notes: Wikipedia
Laban, a centre for contemporary dance in London, has a brown roof specifically designed to encourage the nationally rare black redstart. The Black Redstart (Phoenicurus ochruros) is a small passerine bird in the redstart genus Phoenicurus.

## Slide 16: Semi-Intensive
At least 25 % (roof area) of substrate above (or below) 6”
100 – 250 mm substrate
  Greater diversity of plants, compared to extensive
  Still focused on
    low maintenance plants
    Lower weight
Green Roof Centre (2007) The Green Roof Pocket Guide, 2nd Ed.
Notes: http://www.3riverswetweather.org/
Semi-Intensive: Semi-intensive green roofs can be defined as a hybrid between intensive and extensive green roofs, where at least 25 percent of the roof square footage is above or below the six inch threshold. Semi-intensive and intensive green roofs are designed to be used by the public or building tenants as a park or relaxation area. However, they also require greater capital and maintenance investments than extensive green roofs.

## Slide 17: Semi-Intensive
greeningthecity.files.wordpress.com
Germany

## Slide 18: Semi-Intensive
www.greenroofs.com
Chicago City Hall (2001)
Notes: Project Name: Chicago City Hall Year: 2001 Owner: City of Chicago, Dept of Environment Location: Chicago, IL, USA Building Type: Municipal/Government Type: Semi-Extensive, Test/Research System: Single Source Provider Size: 20300 sq.ft. Slope: 1.5% Access: Accessible, Private Submitted by: Linda S. Velazquez Designers/Manufacturers of Record: Greenroof System: Roofscapes, Inc. (now Roofmeadow) Roofscapes Contractor: Church Landscape Landscape Architect: Conservation Design Forum Architect: McDonough + Partners Project Engineer: Roy F. Weston, Inc. General Contractor: Bennett and Brosseau Roofing Waterproofing: Sarnafil Greenroof Consultant: J?rg Breuning, Green Roof Service LLC

## Slide 19: Green Roof Benefits
Increase life of roof membranes
  Reduce UV & Mechanical damage
  2 – 3 times greater life span
    Roof can last building life time
Energy savings
  Can reduce air conditioning needs by up to 75 %
    Better Insulated
    Evapotranspiration cooling
Green Roof Centre (2007) The Green Roof Pocket Guide, 2nd Ed.

## Slide 20: Benefits
Reduce storm water
  Less costly than traditional systems
Reduce urban heat island effect
Meet green building standards
Meet planning requirements
Some construction wastes can be incorporated into substrate
Increase property value
Green Roof Centre (2007) The Green Roof Pocket Guide, 2nd Ed.

## Slide 21: Cost Factors
Type of green roof
Extra support structure (Intensive)
Engineering fees
Pitch, edging and roof details
  guttering, skylights,…
Roof Size
  economy of scale
Time of year and type of planting
Building height - Crane
Maintenance, irrigation and access
Green Roof Centre (2007) The Green Roof Pocket Guide, 2nd Ed.

## Slide 22: Cost
As much as 2x cost of waterproofing & insulating standard roof
Green Roof Centre (2007) The Green Roof Pocket Guide, 2nd Ed.
assets.nydailynews.com

## Slide 23: Maintenance
Annual removal of unwanted weeds & saplings
Annual clearing of drainage outlets
  Same as traditional roofs
Irrigation in case of drought
Best to pay installer maintain for ~2 years, until plants established
Green Roof Centre (2007) The Green Roof Pocket Guide, 2nd Ed.

## Slide 24: Structural Support
Extensive green roofs fall within load of standard roofs
Type | Load per area (kg/m2)
Gravel Surface | 90 - 150
Paving Slabs | 160 - 220
Extensive green roof | 60 - 150
Intensive green roof | 200 - 500
Green Roof Centre (2007) The Green Roof Pocket Guide, 2nd Ed.

## Slide 25: Pitch
Any pitch is possible
  Above 9.5 care must be take to keep substrate in place and retain water
  Cross battens can be used up to 35
    Closer together as pitch increases
Green Roof Centre (2007) The Green Roof Pocket Guide, 2nd Ed.
node1.ecogeek-cdn.net

## Slide 26: Components
www.greenroofplan.com
Vegetation
Substrate
Drainage / Aeration / Water Storage / Root Barrier
Insulation
Membrane Protection & Root Barrier
Roofing Membrane
Structural Support
Green Roof Centre (2007) The Green Roof Pocket Guide, 2nd Ed.
www.greenroofplan.com

## Slide 27: Planting Options
Pre-grown Mats
  Cover established fast, highest cost, low diversity
Plugs
  Lower cost, cover takes a bit longer, some plants may not be available
Seeds or cuttings
  Low cost, 1-3 years to establish, sow in fall/spring
Natural Colonization
  Lowest cost, high biodiversity, aesthetics may suffer, longest time to establish
Green Roof Centre (2007) The Green Roof Pocket Guide, 2nd Ed.

## Slide 28: Installation
Modular
  Trays
Layers
www.vegetalid.us
Trays

## Slide 29: ESRI Canada - Garden in the Sky
www.greenroofs.com
Trays!
Notes: Project Name: ESRI Canada's Garden in the Sky Year: 2009 Owner: ESRI Canada Location: Toronto, Canada Building Type: Corporate Type: Extensive & Intensive System: Single Source Provider Size: 7500 sq.ft. Slope: 1% Access: Accessible, Private Submitted by: Josephine Chan, ESRI Canada Designers/Manufacturers of Record: Landscape Architect: Scott Torrance Landscape Architect Inc. Landscape Contractor/Installation: Gardens in the Sky Modular Greenroof System: LiveRoof Hybrid

## Slide 30: Layers
www.hvcnyc.com

## Slide 31
Lincoln Center, NYC
geosyntheticsmagazine.com

## Slide 32: Lincoln Center, NYC
Geocells
geosyntheticsmagazine.com

## Slide 33
Lincoln Center, NYC
geosyntheticsmagazine.com