## Slide 1: Stormwater
Introduction
Bioinfiltration
  Stephen Duda
Porous Concrete
  Douglas Cleary
upload.wikimedia.org

## Slide 2: Introduction
Hydrologic Cycle
Watersheds
Implications with Development
Stormwater Management
  History
  Importance

## Slide 3: Hydrologic Cycle
http://ga.water.usgs.gov/edu/watercycle.html

## Slide 4: Watersheds
Groundwater Storage
Precipitation
Runoff
Evapotranspiration
Groundwater Withdrawals
http://science.howstuffworks.com/environmental/conservation/issues/watershed1.htm

## Slide 5: Storm Water
Pre development
  Trapped in puddles, or
  Overland flow impeded by vegetation, and
  Infiltration into ground
  Plenty of evapotranspiration
  Stream Result:
Post development
  Impervious surfaces reduce all of these
  Stream Result:

## Slide 6: Land Use Changes
Image source: Maryland DEP

## Slide 7: Stream Flow
Flow
Time

## Slide 8: Early Stormwater Management
http://www.acogok.org/Programs_and_services/Water_Resources/Storm_Water.asp
http://www.cityofpa.us/stormwater.htm
Collect
Convey
Dump

## Slide 10: Stormwater Quantity
enviroloknw.com

## Slide 11: Stormwater Quantity
enviroloknw.com

## Slide 12: Stormwater Pollution
http://www.flickr.com/photos/columbiariverkeeper/6153168831/
http://www.niskayuna.org/Public_Documents/NiskayunaNY_DPW/Stormwater

## Slide 13: Stormwater Pollutants
Pollutant | Typical Concentration
Total Suspended Solids | 80 mg/L
Total Phosphorus | 0.30 mg/L
Total Nitrogen | 2.0 mg/L
Total Organic Carbon | 12.7 mg/L
Cadmium | 0.002 mg/L
Copper | 0.010 mg/L
Lead | 0.018 mg/L
Zinc | 0.14 mg/L
Chlorides (winter only) | 0.230 mg/L
NJ Stormwater BMP

## Slide 14: Stormwater Pollution
Saint Lucie Inlet Florida
http://www.cityofpsl.com/npdes/
Stormwater pollution shown on left

## Slide 15: What can we do?

## Slide 16: Stormwater Options
Outdated
  Collect, convey, dump in stream
Traditional
  Retention / Detention Pond
  Dry Well
More Recent
  Bioinfiltration Basin / Rain Garden
  Porous Pavement

## Slide 17: Retention Pond
Notes: Retention Basin - a storage site similar to a detention basin but the water in storage is permanently obstructed from flowing downstream. -http://wordnetweb.princeton.edu/perl/webwn?s=retention basin
Most are detention basins, less effective in protecting streams when considered on a watershed basis.

## Slide 18: Detention Basin
iowacedarbasin.org

## Slide 19: Retention/Detention Basins
Typical Pollutant Removal Rates | 
Detention Basin | 
TSS | 40 - 60%
Phosphorus | 20%
Nitrogen | 20%
Retention Basin | 
TSS | 50 – 90%
Phosphorus | 50%
Nitrogen | 30%

## Slide 20: Dry Well

## Slide 21: Bioinfiltration Basin
www.geocaching.com

## Slide 22: Parking Lot
dnr.wi.gov
Wisconsin DNR

## Slide 23: Bioretention Swale
www.esc.rutgers.edu
Notes: A shallow troughlike depression that carries water mainly during rainstorms or snow melts. - www.thefreedictionary.com

## Slide 24: Road-Side
dnr.wi.gov
Wisconsin DNR

## Slide 25: Under Construction
www.jjaconstruction.com

## Slide 26: Plants
Raydons Favorite Aster
Northwind Switchgrass
Seaside
Goldenrod
Dark Ponticum
Bee Balm
Shenandoah
Switchgrass
Orange
Coneflower

## Slide 27: Bio-Infiltration Basins
Typical Pollutant Removal Rates | 
TSS | 90%
Phosphorus | 60%
Nitrogen | 50%

## Slide 28: Economics http://www.ipa.udel.edu/wra/docs/EconomicValueStormwaterDelawareDraftSummary.pdf
California: 1,000 trees reduce stormwater runoff by 1M gallons
Denver: 0.1 ac bioinf basin costs 17% less than traditional retention pond
Philadelphia: every $1 off green stormwater management saves $2
Seattle: green stormwater management costs $280,000 per block
  versus $425,000 for traditional
Notes: California: 1,000 trees reduce stormwater runoff by 1 million gallons & save $7,000
Denver: 0.1 ac bioretention basin cost $75,976, 17% less than traditional stormwater pond
Philadelphia: every $1 spent on green stormwater management saves $2
Museum of Science in Portland, Oregon: saved $78,000 in stormwater management by constructing green stormwater structures
Seattle: green stormwater management costs $280,000 per block
  versus $425,000 for traditional stormwater management

## Slide 29: Rowan University

## Slide 30: Rowan University

## Slide 31: Rowan University

## Slide 32: Effectiveness
November 8, 2012 |  |  |  | 
 |  | First Flush | Lysimeter | Percent Reduction
TSS (mg/L) |  | 37.3 | 12.7 | 66%
Phosphorus (mg/L) |  | 0.98 | 0.41 | 58%
Nitrogen (mg/L) |  | 3.00 | 0.60 | 80%
Zinc (mg/L) |  | 0.06 | 0.05 | 17%

## Slide 33: Bio-Infiltration Basin Design Basis
Output = Infiltration through basin bottom
  Assume  constant rate, as soon as basin begins to fill
Input = Runoff from contributing area
  Q = P =
  Ia =
  S =
Q =
for P ≤ Ia
for P > Ia
0
{
(P – Ia)2
P - Ia + S
Notes: Runoff begins before maximum retention
Write on side board

## Slide 34: More Equations
Ia = 0.2 S
  (Some say more like Ia = 0.05 S)
S = 1000/CN – 10
  CN = Curve Number
    Empirical parameter for predicting runoff or infiltration
    Unitless, range: 0 to 100
    Lower number  more permeability
[P – 0.2(1000/CN – 10)]2
P + 0.8(1000/CN – 10)
Q =
Notes: Method was done for internal use of Soil conservation service. Original work / data a bit obscure.
Ia = 0.05 S results in different design equations for CN and Q

## Slide 35: Curve Number Chart https://engineering.purdue.edu/mapserve/LTHIA7/documentation/scs.htm
Soil Type | Infiltration Rate
A | > 0.3 in/hr
B | 0.30-0.15 in/hr
C | 0.15-0.05 in/hr
D | 0-0.05 in/hr
Proper selection of CN is very important!
More CN tables
Beyond scope of this course
Notes: The runoff curve number (also called a curve number or simply CN) is an empirical parameter used in hydrology for predicting direct runoff or infiltration from rainfall excess - Wikipedia

## Slide 36: Equations
Vr = Q  Al
  Vr = Volume of Runoff; Al = Area of Lot;
    Ignores  ALL rain falling on basin enters basin
Vi = I  T  Ab
  Vi = Volume of Infiltration During Storm; I = Infiltration rate; T = Storm Duration, Ab = Area of Basin
  Vb = Volume of Basin = Vr – Vi
Db = Depth of Basin = Vb / Ab

## Slide 37: Bio-Infiltration Basin Example
Determine bio-infiltration basin depth
  1. Undeveloped, wooded, 1 acre
  2. Residential, Two ½ acre lots
Lot Area
Basin
Notes: Don’t need a basin for undeveloped wooded, included just to see difference.

## Slide 38: Given Information
Lot Area, Al = 1 acre
Basin Area, Ab = 0.10 acre
Max Basin Depth (must drain in 72 hr)
  Infiltration Rate = I = 0.5 in/hr (assumed)
  Max Basin Depth = 72 hrs * 0.5 in/hr = 36 inches
Example Design Storm  Hurricane Irene
  Precipitation = P = 6 in; Time = T = 18 hr
Bio Basin Example
Notes: Regulations – must drain in 72 hours

## Slide 39: Undeveloped, Wooded
Curve Number = CN = 30
Pot. Max. Retention = S = (1000/CN) – 10
  S =
Init. Abstraction
  Ia =
Runoff = Q = (P – 0.2S)2/(P + 0.8S)
  Q =
  Very low, do not need a basin
Bio Basin Example

## Slide 40: Residential, Two ½ acre lots
Curve Number = CN = 54
Pot. Max. Retention = S = (1000/CN) – 10
  S =
  Init. Abstraction
    Ia =
Runoff = Q = (P – 0.2S)2/(P + 0.8S)
  Q =
Bio Basin Example

## Slide 41: Residential Continued
Volume of Runoff
  Vr =
Volume of Infiltration
  Vi =
Volume of Basin
  Vb =
Depth of Basin
  Db =
Bio Basin Example

## Slide 42: Porous Pavers
extension.umd.edu
Porous Pavement
Notes:   Porous Pavement (Mass Low Impact Development Toolkit)
    Porous asphalt and pervious concrete appear to be the same as traditional asphalt or concrete pavement. However, they are mixed with a very low content of fine sand, so that they have 10%-25% void space and a runoff coefficient that is almost zero.
    Paving stones (aka unit pavers) are impermeable blocks made of brick, stone, or concrete, set on a prepared sand base. The joints between the blocks are filled with sand or stone dust to allow water to percolate downward. Runoff coefficients range from 0.1 – 0.7, depending on rainfall intensity, joint width, and materials. Some concrete paving stones have an open cell design to increase permeability.
    Grass pavers (aka turf blocks) are a type of open-cell unit paver in which the cells are filled with soil and planted with turf. The pavers, made of concrete or synthetic, distribute the weight of traffic and prevent compression of the underlying soil. Runoff coefficients are similar to grass, 0.15 to 0.6.

## Slide 43: Porous Pavement
upload.wikimedia.org

## Slide 44: Concrete
Porous
  Cement
  Large Aggregate
  Result:
Normal
  Cement
  Large Aggregate
  Small Aggregate
  Result: few voids
archive.inside.iastate.edu

## Slide 45
images.huffingtonpost.com

## Slide 46
www.lowimpactdevelopment.org
Notes: Permeable Pavement: Permeable pavement comes in four forms: permeable concrete, permeable asphalt, permeable interlocking concrete pavers, and grid pavers. Permeable concrete and asphalt are similar to their impervious counterparts but are open graded or have reduced fines and typically have a special binder added. Methods for pouring, setting, and curing these permeable pavements also differ from the impervious versions. The concrete and grid pavers are modular systems. Concrete pavers are installed with gaps between them that allow water to pass through to the base. Grid pavers are typically a durable plastic matrix that can be filled with gravel or vegetation. All of the permeable pavement systems have an aggregate base in common which provides structural support, runoff storage, and pollutant removal through filtering and adsorption.

## Slide 47: Porous Pavement Storage & Infiltration
www.capecodgroundwater.org

## Slide 48: Typical Profile
Porous Concrete
Storage (Typical void space = 15 %)
Subbase – Compacted Stone Aggregate
Storage
High void space, up to 40 %
Subgrade – Compacted Soil
Infiltration
Looking for infiltration rate ~ 0.5 in/hr

## Slide 49: Porous Pavement Benefits

## Slide 50: Passive versus Active
Passive
  Only handles rain that falls on the porous pavement
Active
  Can handle runoff from surrounding areas

## Slide 51: Rainfall Duration
Design can be based on:
  Precipitation during 24 hour period
  Precipitation during 2 hour period
Design storm depends on how often one can accept system overflow
  Every two years? Five? Ten?

## Slide 52: Glassboro
Recurrence Interval, Yr | 2 Hour Precipitation, in | 24 Hours Precipitation, in
2 | 1.75 | 4.26
10 | 2.55 | 5.08
50 | 3.41 | 7.39
And storms are getting bigger as a result of climate change

## Slide 53: Design Basis
Permeability of Porous Concrete
  Typically NOT an issue: 288 in/hr!
Storage Capacity
  Porous Pavement – Typical is 15 % porosity
  Subbase – as high as 40 % porosity (#67, 1” Top Size)
Infiltration into Subgrade
  Typical rule of thumb is the subgrade should infiltrate ~0.5 in/hr
System should drain within 5 days
  I’ve seen specifications of 2 – 3 days as well
Notes: We assume the bottom of subbase is level!

## Slide 54: Active Porous Concrete Example
Given
  Contributing area is as big as porous pavement area
    Surrounding contributing area is impervious
    What if it was not?
  Porous concrete is 4 in thick with 15 % porosity
    Dc = 4 in; Pc = 0.15
  Subbase has 25 % void space
    Psb = 0.25
  Subgrade infiltration rate is 0.5 in/hr
    I = 0.5 in/hr
  Design for 2 yr storm
    T2 = 2 hr; P2 = 1.75 in
    T24 = 24 hr; P24 = 4.26 in
Calculate depth of subbase
Contributing Area
Porous Concrete Area

## Slide 55: APC Example Continued
2 hr Rainfall
  Volume stored in Porous Concrete
    Vc =
  Subgrade Infiltration Volume
    VI =
  Volume to be stored in Subbase:
    Vsb =
  Subbase Depth
    Dsb =
Porous Concrete Example

## Slide 56: APC Example Continued
24 hr Rainfall
  Volume stored in Porous Concrete
    Vc =
  Subgrade Infiltration Volume
    VI =
  Volume to be stored in Subbase:
    Vsb =
  Subbase Depth
  Subbase depth controlled by 2 hr storm
Porous Concrete Example

## Slide 57: Pavers
www.stonebiltconcepts.com

## Slide 58: Eco Pavers
4.bp.blogspot.com
static.flickr.com