Example Problem 4-8 from 2nd Edition

POLYMATH 5.0 Results

Equilibrium Conversion of Oxygen  in N2+O2->2NO 20 atm 2700K 02-04-2001

NLE Solution

Variable      Value       f(x)       Ini Guess

X           0.1060004   -1.744E-08    0.02

NT0         0.0361104

NO20        0.0054166

NN20        0.027805

V           4.0E-04

NO2         0.0048424

CO2         12.106021

NNO         0.0011483

NN2         0.0272309

CN2         68.077207

K           0.01

CNO         2.870791

Cto         90.276107

NLE Report (safenewt)

Nonlinear equations as entered by the user

[1] f(X) = K*(CO2*CN2)-CNO^2 = 0

Explicit equations as entered by the user

[1] NT0 = 0.4*20*1.01325e5/1000/8.314/2700

[2] NO20 = 0.15*NT0

[3] NN20 = 0.77*NT0

[4] V = 0.4/1000

[5] NO2 = NO20-NO20*X

[6] CO2 = NO2/V

[7] NNO = NO20*X*2

[8] NN2 = NN20-NO20*X

[9] CN2 = NN2/V

[10] K = 0.01

[11] CNO = NNO/V

[12] Cto = NT0/V

Comments

[1] f(X) = K*(CO2*CN2)-CNO^2

X is defined as conversion of O2

[12] V = 0.4/1000

volume in m^3

Settings

Max iterations 	= 150

Tolerance F 	= 0.0000001

Tolerance X	= 0.0000001

Tolerance min	= 0.0000001

General

Search range:   .03 > X >  .01

number of implicit equations: 1

number of explicit equations: 12

Data file: C:\ACDRIVE\Courses 14 june 2000\Reaction Engineering\Lectures\equilibrium conv_part2original.pol