Femlab Tutoiral: Concentration Distribution in a Porous Catalyst Pellet

Open Femlab and click on the Model Library Tab

Go to the Chemical Engineering Module

Mass Transport

Click on Documentation for the Pellet example

First Shape                                                                 All 3 Shapes

Use the centered circle for the catalyst pellet

Formula: R1*R2*C1+R1*R2

Solution (base case)

Submit at the end of the period:

- Turn in 2-D surface plot of velocity, concentration and concentration gradient. Discuss what each one of these graphs shows.

- Change the Deff and comment on the changes it makes to the process. (Try 3 total)

- Decrease the velocity by a factor of 10 and comment on the changes

- Vary the reaction rate constant, k, as suggested in the tutorial.  Use values of the base case (0.1 m/s and k=100 s-1), 10 and 1000 s-1.  Explain what happens to the average outlet concentration (refer to last lab if you need help).