# HYSYS Chemical Reactions & Reactors

In HYSYS there are 2 basic reactor styles and several subgroups.  In HYSYS Plant 2.2 there are the two ideal reactor models of a CSTR and a PFR.  The CSTR model is a standard algebraic model that has been in simulation packages for a number of years.  The ODE’s of the PFR are a recent addition to simulation packages and are solved by dividing the volume into small segments and finding a sequential solution for each volume.  In these more recent models, these reactors not only include energy balances, but pressure drop calculations are a standard feature for packed bed reactors.

Within each of these reactors there are subsets of how the reactants and products are modeled:

Complete the Tutorial located in the pdf manual:

\\galaxy\public1\chemical engineering\HYSYS\Hysys_doc\HYSYS\Hymenu.pdf

Then go to HYSYS Plant 2.2, Tutorials & Applications, Chapter 5 Chemicals Tutorial

Of relevance to this class are 2 sections of the HYSYS manuals:  These manuals are in adobe pdf format and are located in:

Chemical Reactions:  HYSYS Plant 2.2, Simulation Basis, Chapter 4 Reactions.  This presents the details on using the Reaction Manager to add reaction sets.

Chemical Reactors:  HYSYS Plant 2.2, Steady-State Modeling, Chapter 9 Reactors.

Special Note:  HYSYS Reaction rates are given in units of volume of gas phase.  For example to convert from  units of kgcat to volume of gas:

## Summary of Reactions in HYSYS

| Reaction Type | Description: |
| --- | --- |
| Conversion | Conversion% () |
| Equilibrium | ; equilibrium based on reaction stoichiometry. predicted or specified |
| Gibbs | minimization of Gibbs free energy of all components |
| Kinetic | where the reverse rate parameters must be thermodynamically consistent and rate constants are given by |
| Heterogeneous Catalytic | Yang and Hougen form: This form includes Langmuir-Hinshelwood, Eley-Rideal and Mars-van Krevelen etc. |
| Simple Rate | in which is predicted from equilibrium data. |

Reactor Types:

### 1) CSTR model reactors – Well Mixed Tank-Type

| HYSYS Reactor Name | Reaction Types (See above) |
| --- | --- |
| Conversion Reactor | Conversion () |
| CSTR | Simple Rate, Heterogeneous Catalytic, Kinetic |
| Equilibrium Reactor | ; equilibrium based on reaction stoichiometry. predicted from Gibbs Free Energy specified as a constant or from a table of values |
| Gibbs | minimization of Gibbs free energy of all specified components, option 1) no the reaction stoichiometry is required option 2) reaction stoichiometry is given |

2) Plug Flow Reactor:  Simple Rate, Heterogeneous Catalytic, Kinetic