Reactor Sequencing Example Problem Using the data from P2-8

The liquid phase autocatalytic reaction   is to be carried out in reactors in series.  The volumetric flow rate to be processed is 0.01 m3/min.  You have six reactors available to you.  The rate of reaction as a function of conversion is given to you in Figure P2-8a.  How should the reactors be arranged to achieve maximum conversion?  What is the maximum conversion possible?

| Reactor | Volume (m3) | Residence Time (min) |
| --- | --- | --- |
| PFR | 0.02 | 2 |
| PFR | 0.03 | 3 |
| PFR | 0.06 | 6 |
| CSTR | 0.02 | 2 |
| CSTR | 0.025 | 2.5 |
| CSTR | 0.06 | 6 |

Solution:

From manual Digitization of the Graph of Figure P2-8a

| conversion | C_invr |
| --- | --- |
| 0 | 10 |
| 0.05 | 15 |
| 0.1 | 20 |
| 0.15 | 35 |
| 0.2 | 43 |
| 0.25 | 48 |
| 0.3 | 50 |
| 0.35 | 47 |
| 0.4 | 42 |
| 0.45 | 36 |
| 0.5 | 30 |
| 0.6 | 17 |
| 0.65 | 15 |
| 0.7 | 17 |
| 0.72 | 18 |
| 0.74 | 20 |
| 0.75 | 24 |
| 0.78 | 30 |
| 0.8 | 35 |
| 0.815 | 40 |
| 0.8212 | 41.5 |
| 0.83 | 44.29 |

Reactor Sequencing:  Alternate Solution Method for In-Class Example

Numerical Integration using POLYMATH

Data Table:

Numerical Integration using Analysis Feature of POLYMATH

Numerical Integration using POLYMATH data table:  Analytical Integration of a Polynomial

ODE solver

Numerical Integration using Analysis Feature of POLYMATH

Numerical Integration using POLYMATH data table:  Analytical Integration of a Polynomial

First 2 plug flow reactors

Integrating to get 3+6 min

CSTR 1: