### Civil and Environmental Engineering

CE 421 Wastewater Treatment and Design

Fall 2002

GARDEN CITY WASTEWATER TREATMENT PLANT DESIGN PROJECT

Garden City is situated near Rose Creek, as seen on the attached map. You are planning to design a new wastewater treatment plant for Garden City. The first step in this process is to project future population over the expected useful life of the plant. For this purpose, you are to estimate the population for Garden City for the year 2030. You have the following US census data available:

| Year | Population |
| --- | --- |
| 1940 | 32,927 |
| 1950 | 34,666 |
| 1960 | 39,096 |
| 1970 | 55,820 |
| 1980 | 67,867 |
| 1990 | 79,662 |

a. Prepare the appropriate graphs for calculating each of the following 4 models for the population for Garden City:

- Linear model

- Exponential model

- Decreasing Rate of Increase Model (assume 100,000 as a maximum population for Garden City)

- Decreasing Rate of Increase Model (assume 200,000 as a maximum population for Garden City)

- Show the calibrated model equation for each of these 4 models.

- Show the predicted population based on all 4 of these models on the same graph. The x-axis should cover the time period from 1940 to 2040. Also on this graph show the known Garden City population from the above 6 census years.

- Present a table showing the four projections (from the 4 models) for Garden City’s population in the year 2030.

- Discuss which prediction you think is the most reliable, and why.

The following new industries have also been projected for moving into Garden City:

| Industry | Average Flowrate MGD |
| --- | --- |
| Pet Food | 0.5 |
| Potato Processing | 1.0 |
| Cheese | 0.75 |

The wastewater treatment plant will discharge into Rose Creek, which flows into the Delaware River.  The NJDEP has set the following permit limits:

| PARAMETER | AVERAGING PERIOD | EFFLUENT LIMITATIONS |
| --- | --- | --- |
| Flow (MGD) | Monthly Average Daily Max | Monitor and Report |
| BOD5 mg/L CBOD5 mg/L | Monthly Average Weekly Average Monthly Average Weekly Average | 30 mg/L 30 mg/L 20 mg/L 20 mg/L |
| Total Suspended Solids mg/L | Monthly Average Weekly Average | 30 mg/L 45 mg/L |
| pH | Minimum Maximum | 6.0 9.0 |
| Ammonia (Total as N) mg/L | Monthly Average Daily Max | 0.5 mg/L 0.5 mg/L |
| Temperature | Monthly Average Minimum Maximum | Monitor and Report |
| Chlorine Produced Oxidants mg/L | Daily Max | 0.074 mg/L |

Plant Characteristics:

Secondary Treatment Plant with Activated Sludge Process

Beneficial Reuse of Sludge; Sludge produced = Class A Biosolids

Beneficial Reuse of Wastewater – Garden City Golf Course (20 acres)

Plant design:

Plant design indicates a full thorough design of all unit operation processes (physical, chemical or biological) with professional drawings indicating dimensions and relevant design information such as flow rate, hydraulic and BOD/SS loading, detention times, sludge production in lbs/day, aeration requirements, efficiency etc.  Primary treatment should indicate what technology would be used for grit removal (screening, comminution, aerated grit chamber etc.) with design calculations and drawings or relevant vendor pictures.  Chemical processes should indicate names of chemicals and the chemical requirement in lbs/day for the process.

Recommended References:

Metcalf and Eddy, Inc., Wastewater Engineering: Treatment, Disposal, and Reuse, 3rd Ed., McGraw-Hill Book Co., Inc., Boston, MA, 1991, 2002

Crites, Ron and George Tchobanoglous, Small and Decentralized Wastewater Management Systems,  McGraw-Hill Book Co., Inc., Boston, MA, 1998.

Qasim, Syed, Wastewater Treatment Plants: Planning, Design, and Operation, HWR Publishers, 1985.

Warren Viessman, Jr. and Mark Hammer, Water Supply and Pollution Control, 6th Ed., Harper and Row Publishers, 1998.

Ray, B.T.,  Environmental Engineering. PWS Publishing Co., 1995.

APHA, AWWA, WPCF, Standard Methods for the Examination of Water and Wastewater, APHA, 1989 or later.

Sawyer, McCarty & Parkin, Chemistry for Environmental Engineering, McGraw Hill, 1994.

AWWA, Water Quality and Treatment, Amer. Wat. Wrks. Assn., 1990

Unit Operations and Processes in Environmental Engineering, 2nd Edition, Tom D. Reynolds and Paul A. Richards, PWS Publishing Co., 1996.

Environmental Engineering: A Design Approach, Arcadio P. Sincero. Sr.and Gregoria A. Sincero, Prentice-Hall, 1996.

Ten State Standards for Wastewater Facilities

Industrial water pollution control / W. Wesley Eckenfelder, Jr.,McGraw-Hill, NY, 1999.

Vesilind, P. A., Treatment and Disposal of Wastewater Sludges, Revised Ed., Ann Arbor Science, 1979.

Useful Websites for Virtual Tours

http://yorkcity.org/cityservices/wwtp/

http://www.cityofws.org/ellege/index.htm

http://www.state.sd.us/denr/DES/surfacewater/virtual.htm

http://www.nbif.org/education/env-engr/wstwtr_tour/wwtour.html

http://www.statweb.org/pond/fieldtrips3.html

http://www.ci.quincy.il.us/sanhome/sewer.html

http://www.lacsd.org/waswater/wrp/sjc.htm

New Jersey Websites

Water Environment Association http://www.njwea.org/

Passaic Valley Sewerage Authority  http://www.pvsc.com/

Camden County MUA http://www.ccmua.org

Cape May County MUA http://www.acmua.orcom/

Software

Activated Sludge Simulation  http://attila.stevens-tech.edu/~dvaccari/esim.html

http://www.ce.siue.edu/CIVIL/default.htm

Airstripper Design http://www.ce.cmu.edu/~dzombak/asdc1.html

Biofilm Model http://www.ce.utexas.edu/prof/speitel/biofilm/biofilm.html

Trickling Filter  http://www.engr.psu.edu/ce/enve/tf.htm

Java based Activated Sludge Simulator  http://www.syscon.uu.se/~psa/

Chemical Engineering Fundamentals In Biological Systems http://www.engin.umich.edu/labs/mel/Bio/BioFlyer.html

Lecture  Slides and Notes

http://www-ec.njit.edu/~hsieh/ene669.html

http://civil.engr.siu.edu/415/

http://www.ecs.umass.edu/cee/reckhow/courses/370/

Virtual lab http://civil.engr.siu.edu/nsflab/

Original Equipment Manufacturers

http://www.usfilterenvirex.com/

REGULATORY

## Wastewater Engineering Design Guidance, Fact Sheets, and Technical Review and Approval (Minnesota Water Pollution Control Agency)

This site has useful information for design.

http://www.pca.state.mn.us/water/wastewater-engineering.html

New Jersey

Surface Water Discharges http://www.state.nj.us/dep/dwq/sw.htm

Biosolids http://www.state.nj.us/dep/dwq/sludge.htm

Database for all NJ WWTP with surface discharge http://www.state.nj.us/dep/dwq/database.htm

EPA Biosolids

http://www.epa.gov/owm/bio.htm