##### ECOMMS			 	Final Exam		          		April 30, 2007

#### Spring 2007 							               11:00AM– 1:00PM

Student’s Name:

DIRECTIONS: This exam consists of three parts – Part A, Part B and Part C. Answer all questions in all three parts. This exam is OPEN TEXTBOOK/ NOTES/ CALCULATOR, CLOSED COMPUTER/WEB. Remember to specify UNITS for all answers. Use proper NOTATION. Show ALL WORK.

Part A (4 questions @ 10 points each = 40 points)

- A 1-Kz single-tone modulated standard-AM signal has a modulation index of 85%, a carrier amplitude of 100-V and a carrier frequency of 840-kHz.

  - Write down the time-domain expression for the AM signal.

  - Write down the frequency-domain expression for the AM signal.

  - Sketch the spectrum of the AM signal.

  - Calculate the modulation efficiency.

  - Calculate the transmission bandwidth.

- A Huffman-tree is shown in Figure 2 for coding the symbols A through G; the occurrence probability associated with each symbol is also indicated.

###### Figure 2

- What are the individual code words and code lengths for each of these symbols?

- What is the coding efficiency?

- If each of these symbols were equiprobable, would you agree that a fixed length code is about as efficient as any code can be? Give reasons for your answer.

- If each of these symbols were equiprobable, how many source symbols should the source generate for the coding efficiency to be 100 percent?

- Speculate on the state of communications technology in the future. In particular, predict the products and services that will be available to an average consumer in:

  - 2017

  - 2057

  - 2107

- Discuss the trade-offs associated with using multi-level digital baseband signaling for bandpass digital communications.

Part B

- You are required to capture and perform spectral analysis on an AF signal that is bandlimited to 5-kHz. The spectral resolution should be such that the user can distinguish frequencies that are at least 20-Hz apart. You are provided with an HP54645A Oscilloscope (which does NOT support FFT displays) connected to a PC. The PC supports Agilent IntuiLink Scope and Matlab. Design a waveform capture and spectral analysis strategy in the steps outlined below:

- What time window, T, should be set in the oscilloscope for capturing the AF signal? Available options are 10 ms, 100 ms, 1 s and 10 s.

- How many points should be captured? Available settings in IntuiLink Scope include 500 points, 1000 points, 2000 points and 4000 points.

- Write a Matlab program that:

  - Reads in the file containing time and amplitude information from the captured AF signal.

  - Computes the sampling frequency of the time-domain signal.

  - Computes the FFT of the time-domain signal.

  - Displays that part of the computed amplitude spectrum that represents the CFT of the AF signal.

(20 points)

Part C

- Trace Contaminant Detector

You have been hired as the lead systems engineer by a start-up company that has just secured a contract from the US Department of Homeland Security. The project is to design and build a Trace Contaminant Detector (TCD) to detect the presence of extremely small quantities of biological and/or chemical hazards in an airport security environment. The heart of the sensor system is a 16-channel Quartz Crystal Microbalance (QCM) array.

Each QCM consists of a quartz crystal coated with an adsorptive surface along with a pair of Au electrodes. The adsorptive surface is specific to a single analyte and allows a minute amount (a few nanograms) of the contaminant to adhere to it; thus changing the mass of the crystal structure. This change in mass causes a proportional shift in the resonant frequency of the quartz crystal. The mass of the adhering layer is calculated by using the Sauerbrey relation:

m = C f						(1)

where C = 17.7 ng Hz-1 cm-2 for a 5 MHz quartz crystal. The QCM-array consists of 16 separate QCM structures, each with a 14 mm diameter quartz crystal, and each responding to a specific biological or chemical contaminant.

Perform a system-level design of the TCD device. Your device must output a digital bitstream that allows for:

- The display of the detected quantity of each of the 16 contaminants; and,

- A network interface to a remote host for data analysis and archival.

Other desired device specifications are:

| Mass resolution, ng | 3 |
| --- | --- |
| Maximum mass load, g | 90 |
| Output voltage range, V | ± 4.0 |

Your system-level design should not focus on individual components; rather, it should provide block diagrams of systems and subsystems with specified I/O characteristics. Credit will be given for design simplicity, functionality and adherence to current communications standards.

(40 points)

# Text boxes

A: 3/8

B: 3/16

C: 3/16

D: 1/8

E: 1/16

F: 1/32

G: 1/32