## Slide 1: Digital Image Processing ECE.09.452/ECE.09.552
Dr. Shreekanth Mandayam
Electrical & Computer Engineering
Rowan University
Spectral Filtering

## Slide 2: Plan
Image Spectrum
    2-D Fourier Transform (DFT & FFT)
    Spectral Filtering
Lab 2: Spatial and Spectral Filtering

## Slide 3: DIP: Details

## Slide 4: Noise Models
SNRg = 10log10(Pf/Pn)
Power Variance (how?)
SNRg = 10log10(sf2/ sn2)
f(x,y)
g(x,y)
n(x,y)
S
Degradation Model: g = f + n

## Slide 5: Noise Models
N(0,1): zero-mean, unit-variance, Gaussian RV
Theorem:
  N(0,s2) = sN(0,1)
  Use this for generating normally distributed r.v.’s of any variance
>>imnoise

## Slide 6: Image Preprocessing
Enhancement
Restoration
Spatial
Domain
Spectral
Domain
Point Processing
>>imadjust
>>histeq
Spatial filtering
>>filter2
Filtering
>>fft2/ifft2
>>fftshift
Inverse filtering
Wiener filtering

## Slide 7: Recall: 1-D CFT
Continuous Fourier Transform (CFT)
Frequency, [Hz]
Amplitude
Spectrum
Phase
Spectrum
Inverse Fourier Transform (IFT)

## Slide 8: Recall: 1-D DFT
Discrete Domains
  Discrete Time: k = 0, 1, 2, 3, …………, N-1
  Discrete Frequency: n = 0, 1, 2, 3, …………, N-1
Discrete Fourier Transform
Inverse DFT
Equal time intervals
Equal frequency intervals
n = 0, 1, 2,….., N-1
k = 0, 1, 2,….., N-1

## Slide 9: How to get the frequency axis in the DFT
The DFT operation just converts one set of number, x[k] into another set of numbers X[n] - there is no explicit definition of time or frequency
How can we relate the DFT to the CFT and obtain spectral amplitudes for discrete frequencies?
(N-point FFT)
n=0 1 2 3 4 n=N
f=0 f = fs
Need to
know fs

## Slide 10: DFT Properties
DFT is periodic
X[n] = X[n+N] = X[n+2N] = ………
I-DFT is also periodic!
x[k] = x[k+N] = x[k+2N] = ……….
Where are the “low” and “high” frequencies on the DFT spectrum?
n=0 N/2 n=N
f=0 fs/2 f = fs

## Slide 11: 1-D FFT Demo
>>fft
http://users.rowan.edu/~shreek/fall19/ecomms/demos/dft.m

## Slide 12: 2-D Continuous Fourier Transform
Spatial
Domain
Spatial
Frequency
Domain
v
u
y
x

## Slide 13: 2-D Discrete Fourier Transform
>>fft2
>>ifft2
u=0 u=N/2 u=N
v=N v=N/2 v=0

## Slide 14: 2-D DFT Properties
Conjugate symmetry
  demos/con_symm_and_trans.m
Rotation
  demos/rotation.m
Separability
  demos/separability.m
>>fftshift

## Slide 15: Spectral Filtering: Radially Symmetric Filter
Low-pass Filter
  demos/lowpassf.m
u=-N/2 u=0 u=N/2
v=N/2 v=0 v=-N/2
D0
D(u,v)

## Slide 16: Lab 2: Spatial and Spectral Filtering
http://users.rowan.edu/~shreek/spring20/dip/labs/lab2.html

## Slide 17: Summary