## Slide 1: Density (Compactness)
  Walkable yet enough people to support transit
    40 to 200 acres
    7 to 8 du/acre
      Suburbia = ~2
  Density supports
    Transit service
    Retail shops
    District energy system
  Density protects
    undeveloped & sensitive lands
slanich.zenfolio.com (Gothenburg, Sweden)
streetsblog.net (Cincinnati, Over-the-Rhine)
Farr 2008
Notes: Density > 7 or 8 dwellings/acre
  (Suburbia is ~2 dwellings/acre, not walkable)
Achievable w/ spectrum of housing types
Multifamily to large-lot detached single family
  Reduced building envelope of multifamily dwellings saves 30-35 % HVAC
  Center w/ apartments above stores
    “Built in” customers
    Walking replaces car trips
District energy systems
Less paved area / person
Save natural areas

## Slide 2: Low Density Residential
www.ontarioplan.org
Notes: (2.1 - 5.0 du/acre)

## Slide 3: Medium Density Residential
www.ontarioplan.org

## Slide 4: High Density Residential
High Density Residential (25.1 - 45.0 du/ac)
The High Density Residential land use designation allows between 25.1 and 45.0 dwelling units per acre and accommodates single-family attached dwellings, including stacked flats and mid-rise and high-rise residential complexes.
www.ontarioplan.org

## Slide 5: NYC Mott Street (Chinatown) c1900
www.businessinsider.com

## Slide 6: High Rise Stacked Flats (75 – 150 + du/acre)
www.architectural-review.com
Paris

## Slide 7: Travel and Density
Chart: People Density (People/acre)
| 5 | 30 | 250
Miles/acre | 150 | 300 | 1000
Mile/Person | 30 | 10 | 4
Farr 2008

## Slide 8: Stormwater Runoff and Density
Houses on One Acre | Imperious Cover (%) | Total Runoff (ft3/yr) | Runoff per Dwelling (ft3/yr)
1 | 20 | 18,700 | 18,700
4 | 38 | 24,800 | 6,200
8 | 65 | 39,600 | 4,950
Farr 2008

## Slide 9
www.eea.europa.eu, 2002