Freshman Clinic II

## Spring 2005                                                                                        Dr. Kauser Jahan

# QUIZ # 2:  WATER TREATMENT

Show all your work.  NO CALCULATIONS NO POINTS!!

Activated carbon is universally used to remove water pollutants.

- Name two properties that make activated carbon an excellent choice as an adsorbent.

- Two types of activated carbon are being used to test their effectiveness in removing compound XX from aquarium water.  Experimental data obtained were plotted to see if the data followed the conventional Freundlich isotherm which is as follows:.

The plots are show below:

`

q  mg/g

Ce  mg/L

  - What is the unit for Kp?  Show how you arrived at this unit.

b)  Which carbon A or B  is more efficient and why?

3.    Freundlich presented the following model for adsorption

This equation can be written as

Dr. Jahan and her students have obtained adsorption data for activated carbon in removal of a contaminant called phenol.  The data was plotted to check if it followed this Freundlich model.

log x/m

log Ce

a)  Does the data follow the Freundlich model?

b) What are the values of the coefficient “n” and “Kp”?

4.  A glass column was packed with activated carbon.  The following information is available:

a) Calculate the volume of the column in cm3.

  - The volume occupied by the carbon is 0.37xTotal volume of the column.  Calculate the weight of activated carbon in grams and the surface area of the carbon in m2.

c)  Detention time can be obtained by dividing flowrate Q by the volume of the column.  What is the column detention time in minutes?

  - The column is removing phenol from water.  If the initial concentration of phenol is 2.38 mg/L and the effluent concentration out of the column is 1.45 g/L, what is the percent removal of phenol?

# Text boxes

Column Diameter  2.8 cm

Length of column 40 cm

Flowrate  Q  =  10  cm3/sec

Activated Carbon Density  2.36 g/cm3

Surface Area of carbom 100 m2/g

Area of a circle = r2

Equation of the straight line

y = 0.289 + 1.23x

A

B