GAS TRANSFER STUDY GUIDE

- Name three factors that impact gas transfer of oxygen in water.

Temperature,  Pressure , Salinity

- Which diffuser is better for aeration?  Why?

Kla for Airmax  0.2331 min-1

Kla for Wonder 0.2792 min-1

Therefore Wonder is better as 0.2792> 0.2331

3.  Aeration kinetics can be expressed as follows:

ln(C*-Ct) = ln(C*-Co) – KLa t  where

C* = saturation concentration of oxygen in water (mass/volume)

Ct = oxygen concentration in water at ant time t (mass/volume)

KLa = gas transfer coefficient (time-1)

t= time

Your team has plotted data collected from a gas transfer experiment as shown below and has obtained the equation of the best-fit straight line.

# Text boxes

a) What is the value of KLa in min-1 that can be obtained from this plot?  Write appropriate UNITS!

Slope = Kla = 0.2331 sec-1

= 0.2331 * 60 sec     = 13.9 min-1

Sec         min

- What is the value of Co if the value of C* = 9.5 mg/L

Note Intercept = ln(C*-Co) = 1.9389

Or 			ln (9.5-Co) = 1.9389

Or 			9.5-Co = e1.9389  = 6.951

Or 		Co = 9.5-6.951 = 2.549 mg/L