# CEE 311  Environmental Engineering I                                                            Fall 2012

Dr. Kauser Jahan, P.E.

Laboratory 3:  BIOChemical oxygen demand (BOD)

Objectives:    To measure the Biochemical Oxygen Demand of given wastewater samples.

# Sample Source:

Rowan Pond Water

Background: It takes five days to run a BOD test. Traditional tests are based on the difference between the initial and final DO.

Supplies:  BOD Bottles, DI water, Hach BOD Nutrient Buffer (Cat. #14861-98), Erlenemeyer Flasks

Equipment: Autoclave, Incubator (set at 20oC), Dissolved Oxygen Meters, BOD Stirring Probes

Method:

## Dilution Water

Add 1 pillows of Hach BOD Nutrient Buffer to 19 L of

DI water.  Mix/shake contents for 10 minutes.

Aerate the water overnight to saturate with oxygen

Dilution water contains nutrients (N and P) and

buffers to resist pH changes

### Seeding

Seed the dilution water shortly before adding dilution water to BOD bottles; add to dilution water 3 ml of raw sewage (that has been allowed to stand at ~20oC for ~ 24 hours) per liter of dilution water.  Pipette the wastewater from the top of a wastewater sample.  Mix well.

##### DO Probe Handling

Insert the probe into the BOD bottle.  Turn on stirrer, and wait at least 2 minutes and record value.

Initial D.O.

Allow all wastewater samples to reach ambient temperature before starting.  Always stir or mix samples before pouring.

- Measure and record the initial dissolved oxygen of the dilution water.

- Measure and record the initial DO of each wastewater  (Not required for sample volumes less than 3 mL or if the sample has no DO).

- Use Table 1 to determine the volume of wastewater to be added to the BOD bottle.

- Pipette the specified volumes of wastewater into the BOD bottles.  Use a new pipette for each sample.

- Add dilution water to the BOD bottles after completing pipetting of wastewater.

- Fill each BOD bottle up to the bottom of the ground glass joint on the neck with dilution water.

- Fill a BOD bottle only with dilution water only.  These are the blanks (or controls).

- Add some drops of dilution water on top of the cap to form a water seal.  Cover the cap with parafilm.

- Place bottles in an incubator at 20oC and leave them undisturbed for 5 days.

###### Final DO

- Remove all bottles from the incubator.

- Remove parafilm and invert bottles to break the water seal.

- Measure the mg/l D.O. remaining in the BOD bottles.

PLEASE WASH ALL GLASSWARE WITH SOAP AND TAP WATER.  Final Rinse with DI water.

Data Analysis for BOD determination:

For unseeded samples

BOD5 = (D1 - D2) / P

D1 = Initial D.O.

D2 = 5-day D.O.

P  = Decimal fraction of sample = V/300

V  = Volume in ml of sample added to BOD bottle

For Seeded Samples

BOD5 = [(D1 - D2) - f(B1 - B2)] / P

B1 = Initial D.O. of dilution water

B2 = 5-day D.O. of dilution water

f  = Ratio of seed in sample to seed in control.  If seed is introduced by addition to dilution water, f = 1 - P.

# INDIVIDUAL LABORATORY REPORT

# (Hand written reports will not be accepted.  Use computer spreadsheets and word processors as necessary.  Sample calculations should be presented on engineering paper.)

## Objectives:  Indicate objectives of this laboratory.

Method:   Standard Method 5210B is used for this test.

## Results

- Report raw data in a tabular form.

- Include Excel worksheet showing calculations with formulae and plots if applicable.

- Report results on a separate sheet of paper with appropriate units.

## Discussion

- Indicate with schematic, locations at a WWTP where BOD5 measurements are important.

- Please indicate if your results are reasonable for a wastewater treatment plant.

- What are the limitations of the BOD5 test?

- Why is the 20oC temperature used in this test?

6.  What does the dilution water contain and why does it contain certain compounds?

Table 1: Dilution ranges for pipetting into 300 mL BOD bottles.

| Sample Volume (mL) | Minimum BOD (mg/L) | Maximum BOD (mg/L) |
| --- | --- | --- |
| 1 | 600 | 2400 |
| 3 | 200 | 800 |
| 5 | 120 | 480 |
| 10 | 60 | 240 |
| 30 | 20 | 80 |
| 50 | 12 | 48 |
| 100 | 6 | 24 |
| 200 | 3 | 12 |
| 300 | 2 | 8 |

BOD Data Sheet


Name _________________________

Date _________________________

Laboratory Section _________________________

Treatment Facility _________________________

Initial Date and Time _________________________

Final Date and Time _________________________

| Sample | Influent or Effluent | Volume mL | Initial DO mg/L | Final DO mg/L | DO uptake mg/L | P | BOD mg/L |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | - | - | - | - | - | - | - |
|  | - | - | - | - | - | - | - |
|  | - | - | - | - | - | - | - |
|  | - | - | - | - | - | - | - |
|  | - | - | - | - | - | - | - |
|  | - | - | - | - | - | - | - |
| Dilution Water Blank | - | - | - | - | - | - | - |

EQUIPMENT USED (include model numbers):

# Text boxes

Seeding is only required for samples that do not contain bacteria (e.g., filtered samples, industrial wastewaters).

Already completed

NOTE:  When pipetting wastewaters and adding dilution water, hold the bottle at a 45° angle and allow the liquid to trickle slowly down the sides of the bottle to prevent bubble formation! Stopper each bottle as soon as it is filled.