##### ECOMMS			 	Quiz 2		       	     March 3, 2008

#### Spring 2008 								     12:40 – 1:20 PM

Student’s Name: 								____________

DIRECTIONS: This quiz is CLOSED BOOK/NOTES/COMPUTER/WEB. Calculators are permitted. Remember to specify UNITS for all answers. Use proper NOTATION. Show ALL WORK.

- A rectangular pulse has a width of 1-ms and amplitude of 1-V.

  - Sketch the amplitude spectrum (Continuous Fourier Transform) of this pulse, indicating all amplitudes and frequencies.

  - Sketch the 1,000-point FFT of the pulse, if all the points are sampled over the pulse width of 1-ms. Clearly indicate all the frequencies on the x-axis.

(10 points)

- A carrier signal with an amplitude of 100-V and frequency of 600-kHz is amplitude modulated by a single tone of amplitude 0.85-V and frequency 5-kHz.

  - Write down the time-domain expression for the AM-signal, clearly indicating the carrier component, the upper sideband and the lower sideband.

  - Compute the modulation index and efficiency of this AM transmission.

  - What is the maximum amplitude of the message signal, that is allowed by the FCC? Why does this limit exist?

  - What is the efficiency of the AM transmission, at the maximum allowed message amplitude? Based on this, comment on the efficiency of AM as a method of communications.

(15 points)